## Slide 1
FPGA Applications on Nautilus
Mohammad Sada and Elham Khoda
Sixth National Research Platform (6NRP) Workshop
San Diego Supercomputer Center
January 28th, 2025

## Slide 2
2
The Slides can be found at:
https://github.com/nrp-nautilus/6nrp-fpga

## Slide 3
3
FPGAs

## Slide 4
4
FPGAs
- Field-Programmable Gate Arrays
- Unlike CPUs/GPUs (general-purpose), FPGAs are programmed for specific applications.
- Analogy: CPU = Swiss Army knife, handles variety of tasks, but not optimized. FPGA = Custom-rebuilt machinery, designed for a specific job.
- High Throughput, Low Latency, Energy Efficiency, Flexibility

## Slide 5
5
How Are FPGAs Programmable?
- HDL (Hardware Description Language): FPGAs are programmed using languages like Verilog or VHDL (low-level hardware description).
These languages describe the circuit’s behavior at the logic level, such as AND, OR gates, or complex logic circuits.
- HLS (High-Level Synthesis): Use C/C++ for FPGA programming (via tools like Vitis HLS).
Converts high-level code into hardware designs, making FPGA programming more accessible.
HLS C/C++
Verilog/VHDL
Vitis/Vitis HLS

## Slide 6
6
How Are FPGAs Programmable?
module uart_tx_hello_world (
input clk, // Clock signal (100 MHz)
input rst, // Reset signal
output tx, // UART transmit pin
output reg [7:0] led_out // Optional: To indicate transmission progress
);
// UART settings
parameter BAUD_RATE = 115200;
parameter CLOCK_FREQ = 100_000_000; // 100 MHz clock
// Baud rate generator (generate 115200 baud)
reg [15:0] baud_counter;
reg baud_tick;
// State machine for transmitting UART data
reg [3:0] state; // FSM states (Idle, Start, Data, Stop)
reg [7:0] data_byte; // Byte to be transmitted
reg [3:0] bit_index; // Index of current bit in the byte
reg transmitting; // Indicates if data is being transmitted
// String "Hello World!" (as 8-bit characters)
reg [7:0] message [11:0];
integer i;
// Baud rate counter
always @(posedge clk or posedge rst) begin
if (rst) begin
baud_counter <= 0;
baud_tick <= 0;
end else begin
if (baud_counter == (CLOCK_FREQ / BAUD_RATE - 1)) begin
baud_counter <= 0;
baud_tick <= 1; // Generate baud tick every 1 clock cycle
end else begin
baud_counter <= baud_counter + 1;
baud_tick <= 0;
end
end
end
// State machine to handle transmission
always @(posedge clk or posedge rst) begin
if (rst) begin
state <= 0;
transmitting <= 0;
bit_index <= 0;
data_byte <= 0;
i <= 0;
led_out <= 0;
end else if (baud_tick) begin
case (state)
0: begin // Idle state
if (i < 12) begin
state <= 1; // Start transmission
transmitting <= 1;
data_byte <= message[i]; // Load next character
bit_index <= 0;
led_out <= 1; // Indicate activity on the LED
end
end
1: begin // Start bit
tx <= 0; // Start bit (low)
state <= 2;
end
2: begin // Data bits (8 bits)
tx <= data_byte[bit_index]; // Send each bit
if (bit_index == 7) begin
state <= 3; // After 8 bits, go to stop bit
end else begin
bit_index <= bit_index + 1;
end
end
3: begin // Stop bit (high)
tx <= 1; // Stop bit (high)
state <= 0; // Back to idle
if (transmitting) begin
i <= i + 1; // Move to next character in the string
end
transmitting <= 0;
end
endcase
end
end
// Initialize "Hello World!" message
initial begin
message[0] = "H";
message[1] = "e";
message[2] = "l";
message[3] = "l";
message[4] = "o";
message[5] = " ";
message[6] = "W";
message[7] = "o";
message[8] = "r";
message[9] = "l";
message[10] = "d";
message[11] = "!";
end
endmodule

## Slide 7
7
AMD/Xilinx Alveo U55C

## Slide 8
8
AMD/Xilinx Alveo U55C
PCI Express Interface
Gen3 x16 or 2 x Gen4 x8
Networking
2 x QSFP28 connectors (100 Gb/s each)
Memory
16 GB High-Bandwidth Memory (HBM2)
HBM2 Bandwidth
460 GB/s
Internal SRAM Capacity
43 MB
Internal SRAM Bandwidth
35 TB/s
LUTs
1,304,000
Registers
2,607,000
DSP Slices
9,024
Dimensions
Full Height, Half Length, Single Slot
Power
Maximum: 150W, Typical: 115W

## Slide 9
9
FPGAs and HPC – Use Cases

## Slide 10
10
FPGAs and HPC – Use Cases
1- Machine Learning and AI Acceleration:
- Vitis AI enables using Alveo Versal FPGAs for both inference and fine-tuning.
Converts TensorFlow and PyTorch models into Verilog for FPGA deployment.
- hls4ml converts machine learning models into FPGA-ready HLS designs.
Optimizes machine learning algorithms for FPGA deployment.
Is open-source.
Free and Open-Source and Supported on Nautilus.

## Slide 11
11
FPGAs and HPC – Use Cases
2- FPGAs as SmartNICs
- FPGAs are used as SmartNICs for customizable packet processing at high bandwidth (2x100Gbps).
- Supports P4 programming for custom network processing.
Ideal for high-bandwidth, low-latency networking.

## Slide 12
12
FPGAs on Nautilus

## Slide 13
13
FPGAs on Nautilus

## Slide 14
14
FPGAs on Nautilus
32 FPGAs

## Slide 15
15
FPGAs on Nautilus
HDL
Bitstream
HLS Code
Allocated resources: (Total limits may be over 100 percent, i.e., overcommitted.) Resource Requests Limits -------- -------- ------ amd.com/xilinx_u55c_gen3x16_xdma_base_3-0 4 4
resources:
requests:
amd.com/xilinx_u55c_gen3x16_xdma_base_3-0: 1
limits:
amd.com/xilinx_u55c_gen3x16_xdma_base_3-0: 1

## Slide 16
16
Hands-On Examples

## Slide 17
17
Hands-On Examples
Please go to:
https://github.com/nrp-nautilus/6nrp-fpga