## Slide 1
Agricultural Mobile Robots for Automated Field Data Collection and Analysis
Konstantinos Karydis, PhD
Associate Professor
Electrical and Computer Engineering
University of California, Riverside
kkarydis@ece.ucr.edu
arcslab.org
7th National Research Platform (7NRP) Workshop
May 6, 2026

## Slide 2: Summary of Ongoing Ag Robotics Research
Autonomous Mobility (“Where to Sample?”)
  Joint task and motion planning for optimal sampling
  Realtime and on-the-go reactive sampling
  Tunable (efficiency vs speed) exploration of unknown and obstacle-rich environments
  Field navigation using multi-modal sensory data
  Digital twin creation (See our CitrusFarm Dataset!)
Interactive Intelligence (“How to Sample?”)
  Mechatronics for physical and proximal sampling
  Perception-based actuation and control
  Autonomous ground/aerial mobile manipulation
  Integration of augmented reality interfaces for fluent human-robot interaction

## Slide 3: Today: Automated Data Collection & Analysis
Necessary algorithms for robot-assisted data retrieval
LiDAR-based odometry estimation and mapping
Multimodal sensor fusion for scene understanding
Deploy (semi-)autonomous robots to collect multi-modal field data and use them for various downstream tasks!
Sample downstream tasks
Digital twin creation (multimodal dataset)
Field-scale autonomy (soil ECa mapping)

## Slide 4: Adaptive LiDAR Odometry & Mapping
Two-stage GICP scan matching to register point clouds in unstructured environments
Adaptive approach to effectively handle rough terrain and non-smooth robot motion
Use of a single LiDAR to simplify deployment on autonomous agricultural robots
  Teng, Wang, Chatziparaschis & Karydis, Elsevier Comp. Electron. Agri. 2025

## Slide 5: Adaptive LiDAR Odometry & Mapping
  Teng, Wang, Chatziparaschis & Karydis, Elsevier Comp. Electron. Agri. 2025
Testing at UCR’s agricultural fields
  A: Simple trajectories across fields
  B: Variable challenging trajectories
  C: Various trajectories to benchmark absolute translation error
Feature-based: LeGO-LOAM[2] | ICP-based: KISS-ICP[4]
Continuous-time: CT-ICP[3] | GICP-based: HDL-Graph-SLAM,[5] LOCUS[6]
Evaluation with the Treescope[1] dataset
  Sequence UCM-0523M (mobile platform)
  Sequence UCM-0523U (UAV platform)
Comparisons with various different methods
  >> Data & Code Available! (github.com/UCR-Robotics/AG-LOAM)

## Slide 6: Adaptive LiDAR Odometry & Mapping
  Teng, Wang, Chatziparaschis & Karydis, Elsevier Comp. Electron. Agri. 2025
Our method performs well across cases
Quantitative metric: absolute translation errors (RMSE, meter)
UCR Dataset, Case C

## Slide 7: Adaptive LiDAR Odometry & Mapping
  Teng, Wang, Chatziparaschis & Karydis, Elsevier Comp. Electron. Agri. 2025

## Slide 8: Multimodal Sensor Fusion for Landmark Detection
Main objective: Match the detected tree candidates in with the local tree landmarks and their global representations
Landmark updates when maximum matching probability and decreased entropy
RGN frame
Binary Mask
Projected LiDAR points
on the frame
Obtaining points with
NDVI value -0.3
  Chatziparaschis, Teng, Wang, Peiris, Scudiero & Karydis, IEEE ICRA 2024
Notes: LiDAR-camera fusion to obtain tree geometric traits and georeference on a global map
Entropy-based correspondences for 3D tree cluster matching and localization
Proximal RGN sensing to integrate domain-specific vegetation data for active landmark detection
and matching probability computation: (1)
with (2)
LiDAR-camera fusion to obtain tree geometric traits and georeference on a global map
Entropy-based correspondences for 3D tree cluster matching and localization
Proximal RGN sensing to integrate domain-specific vegetation data for active landmark detection
𝒞_𝑘 and 𝒯_𝑗 matching probability computation: (_ ^𝒌)𝒑_𝒋 =exp⁡(−0.1∙𝑑_ℳ (𝒊_𝑗, 𝑺_𝑗^(−1)))∈[0,1] (1)
ℋ=−∑_𝑗▒(_ ^𝒌)𝒑 ̂_𝒋 ∙〖"log" 〗_ℳ ((_ ^𝒌)𝒑 ̂_𝒋 ) with ∑_𝑗▒(_ ^𝒌)𝒑 ̂_𝒋=1 (2)
𝑁𝐷𝑉𝐼=(𝑁𝐼𝑅 −𝑅𝑒𝑑)/(𝑁𝐼𝑅+𝑅𝑒𝑑)∈ [−1,1]

## Slide 9: Multimodal Sensor Fusion for Landmark Detection
Testing in a custom 2×3 citrus tree farm simulated in Gazebo
  Different tree placement densities (d)
  4𝑚×4𝑚, 5𝑚×5𝑚 and 6𝑚×6𝑚 configurations
  Different paths followed: Straight-line, N-Type, and S-Type
Comparison against Robotic Precision Harvesting (RPH)[8]
Evaluation with our dataset CitrusFarm[7] and at UCR’s agricultural fields
  Chatziparaschis, Teng, Wang, Peiris, Scudiero & Karydis, IEEE ICRA 2024

## Slide 10: Multimodal Sensor Fusion for Landmark Detection
  Chatziparaschis, Teng, Wang, Peiris, Scudiero & Karydis, IEEE ICRA 2024

## Slide 11: Multimodal Sensor Fusion for Landmark Detection
  Chatziparaschis, Scudiero, Sams & Karydis, IEEE ICRA 2026 (To Appear)
Main objective: Develop a lightweight annotation-to-detection framework for real-time multimodal detection
Early-fusion cross-modal annotation pipeline to generate ROI masks
Incremental detection leveraging prior knowledge to refine detection
Accurate in-field vine localization, integrating earlier LOAM and landmark detection algorithms

## Slide 12: Multimodal Sensor Fusion for Landmark Detection
  Chatziparaschis, Scudiero, Sams & Karydis, IEEE ICRA 2026 (To Appear)
Multimodal Raw Input
Minimal Dataset Refinement & Model Training
Initiation of Semantic Masks
Spatial Association and Dataset Generation

## Slide 13: Multimodal Sensor Fusion for Landmark Detection
  Chatziparaschis, Scudiero, Sams & Karydis, IEEE ICRA 2026 (To Appear)
Field experiments: Two settings, one single row (10 trees) and a double row (each row with 7 trees)
Low errors (<0.32m in single row, <0.37 in double row)
High vine detention rates (<80% in single row, >70% in double row)
Single-row: High recall rates across the two vine groups
Double-row: Stable performance in both row detection, despite diverse sunlight and vine occlusions
Experiment | Single Row -vines |  |  | Dual Row -vines
 | Vines 1—5 | Vines 5—10 | Total | 
L2 Error | 0.32m | 0.24m | 0.28m | 0.37m
 | 0.05m | 0.11m | 0.09m | 0.06m
 | 0.05m | 0.12m | 0.1m | 0.07m
 | 60% | 80% | 80% | 71%
Vine Detections | 4 out of 5 | 4 out of 5 | 8 out of 10 | 10 out of 14
Experiment |  |  |  | 
 | Vines 1—5 | Vines 5—10 | Total | 
L2 Error | 0.32m | 0.24m | 0.28m | 0.37m
 | 0.05m | 0.11m | 0.09m | 0.06m
 | 0.05m | 0.12m | 0.1m | 0.07m
 | 60% | 80% | 80% | 71%
Vine Detections | 4 out of 5 | 4 out of 5 | 8 out of 10 | 10 out of 14
Single row
Dual row

## Slide 14: Today: Automated Data Collection & Analysis
Necessary algorithms for robot-assisted data retrieval
LiDAR-based odometry estimation and mapping
Multimodal sensor fusion for scene understanding
Sample downstream tasks
Digital twin creation (multimodal dataset)
Field-scale autonomy (soil ECa mapping)
Deploy (semi-)autonomous robots to collect multi-modal field data and use them for various downstream tasks!

## Slide 15: The CitrusFarm Dataset
Multimodal dataset for robot localization and mapping, and crop monitoring in citrus tree farms
Nine sensing modalities
  Stereo RGB, depth, monochrome, near-infrared and thermal images
  Wheel odometry, LiDAR, IMU, RTK-GPS
Three different fields
Data collected over the span of Summer 2023
Total operation time: 1.7 hrs; total distance: 7.5 km; total data size: 1.3 TB
  Teng, Wang, Song & Karydis, ISVC 2023

## Slide 16: The CitrusFarm Dataset
  Teng, Wang, Song & Karydis, ISVC 2023
Field 1
Field 2
Field 3

## Slide 17: The CitrusFarm Dataset
  Teng, Wang, Song & Karydis, ISVC 2023
Dataset Website
Dataset Repo

## Slide 18: The CitrusFarm Dataset
  Teng, Wang, Song & Karydis, ISVC 2023
Open-source!
Dataset Website
Dataset Repo

## Slide 19: Field-scale Autonomy: Soil ECa Mapping
  Kan, Thayer, Carpin & Karydis, RA-L + ICRA 2021;
  Samanta, Acharya, Chatziparaschis, Scudiero & Karydis, ECPA 2025; Prec. Agri 2026 (In Press)
Main objective: Develop a fully-autonomous navigation pipeline for field traversal and agronomic data collection
  Focus: Soil apparent electrical conductivity (ECa)
Long, continuous operation to capture a field in its entirety
Use of prioritize locations to drive motion planning and improve efficiency
Simplify field representation using graphs
Fusion of informed planning, odometry estimation and mapping

## Slide 20: Field-scale Autonomy: Soil ECa Mapping
  Samanta, Acharya, Chatziparaschis, Scudiero & Karydis, Prec. Agri 2026 (In Press)

## Slide 21: Outlook: Mobile Manipulation For Harvesting
  Liu et al., ICRA 2025; gripper design: Zhou et al., AIM 2024; UAV deployment: Liu et al., ARR 2025

## Slide 22: Acknowledgements
Lab videos and paper presentations: https://www.youtube.com/@arcslab/videos
Collaborators (across discussed and/or ongoing projects)
Elia Scudiero (UCR Env. Science)
Peggy Mauk (UCR / UC ANR)
Amit Roy-Chowdhury (UCR ECE)
Kerry Mauck (UCR Entomology)
ARCS Lab Group Members (current members contributing to discussed projects)
Dimitris Chatziparaschis
Aritra Samanta
Stefano Carpin (UCM EECS)
Thomas Harmon (UCM Civil & Env. Eng.)
Daniele Zaccaria (UCD LAWR)
Anne Visser (UCD Human Ecology)
… and more in ongoing projects!
ARCS Lab Group Members (alumni who contributed to discussed projects)
Dr. Hanzhe Teng (PhD grad Su’24)
Dr. Zhichao Liu (PhD grad Sp’23, postdoc F’24)
Dr. Xinyue Kan(PhD grad Sp’21)
Jingzong Zhou
… and more in ongoing projects!
Pamodya Peiris (MS grad W’26)
Yipeng Wang (MS grad Su’23)
Joy Banik (MS grad Su’24; w/ E. Scudiero)
Recent technical presentation at IEEE RAS AgRa TC: https://youtu.be/ZZlb7OKko_M?si=puV1YB6uzybZAuYA

## Slide 23
Gracefully acknowledging support from:
arcslab.org
Thank you!
Agricultural Mobile Robots for Automated Field Data Collection and Analysis

## Slide 24: References
[1] D. Cheng et al., “TreeScope: An Agricultural Robotics Dataset for LiDAR-Based Mapping of Trees in Forests and Orchards.” In IEEE International Conference on Robotics and Automation (ICRA), 2024
[2] T. Shan & B. Englot, “LeGO-LOAM: Lightweight and Ground-Optimized Lidar Odometry and Mapping on Variable Terrain.” In IEEE/RSJ International Conference on Intelligence Robots and Systems (IROS), 2018
[3] P. Dellenbach et al., “CT-ICP: Real-time Elastic LiDAR Odometry with Loop Closure.” In IEEE International Conference on Robotics and Automation (ICRA), 2022
[4] I. Vizzo et al., “KISS-ICP: In Defense of Point-to-Point ICP Simple, Accurate, and Robust Registration If Done the Right Way.” IEEE Robotics and Automation Letters, 2023
[5] K. Koide et al., “A portable three-dimensional lidar-based system for long-term and wide-area people behavior measurement.” International Journal of Advanced Robotic Systems, 2019
[6] M. Palieri et al., “LOCUS: A Multi-Sensor Lidar-Centric Solution for High-Precision Odometry and 3D Mapping in Real-Time.” IEEE Robotics and Automation Letters, 2020
[7] H. Teng et al., “Multimodal Dataset for Localization, Mapping and Crop Monitoring in Citrus Tree Farms,” in Advances in Visual Computing: 18th International Symposium (ISVC), 2023
[8] E. Jelavic et al., “Robotic precision harvesting: Mapping, localization, planning and control for a legged tree harvester”, Field Robotics, 2022.